SSH Y IP ESTATICA EN RASPBIAN JESSIE

1) Configurar el archivo /etc/network/interfaces

# interfaces(5) file used by ifup(8) and ifdown(8) / # Please note that this file is written to be used with dhcpcd / # For static IP, consult /etc/dhcpcd.conf and 'man dhcpcd.conf' / # Include files from /etc/network/interfaces.d: / source-directory /etc/network/interfaces.d / auto lo / iface lo inet loopback / iface eth0 inet static / address 192.168.2.61/24 / netmask 255.255.255.0 / gateway 192.168.2.1 / dns-nameservers 8.8.8.8 8.8.4.4 / allow-hotplug wlan0 / iface wlan0 inet manual / addres 192.168.2.62/24 / netmask 255.255.255.0 / gateway 192.168.2.1 / wpa-conf /etc/wpa_supplicant/wpa_supplicant.conf / allow-hotplug wlan1 / iface wlan1 inet manual / wpa-conf /etc/wpa_supplicant/wpa_supplicant.conf

2) Agregar a la configuración del dhcp:

$ sudo nano /etc/dhcpcd.conf

# Rapid commit support. / # Safe to enable by default because it requires the equivalent option set / # on the server to actually work. / option rapid_commit / # A list of options to request from the DHCP server. / option domain_name_servers, domain_name, domain_search, host_name / option classless_static_routes / # Most distributions have NTP support. / option ntp_servers / # Respect the network MTU. / # Some interface drivers reset when changing the MTU so disabled by default. / #option interface_mtu / # A ServerID is required by RFC2131. / require dhcp_server_identifier / # Generate Stable Private IPv6 Addresses instead of hardware based ones / slaac private / # A hook script is provided to lookup the hostname if not set by the DHCP / # server, but it should not be run by default. / nohook lookup-hostname / interface eth0 / static ip_address=192.168.2.61/24 / static routers=192.168.2.1 / static domain_name_servers=8.8.8.8 8.8.4.4 / interface wlan0 / static ip_address=192.168.2.62/24 / static routers=192.168.2.1 / static domain_name_servers=8.8.8.8 8.8.4.4

3) Habilitar el SSH: para esto debemos de conectar la raspberry a un monitor por HDMI:

1 down vote	I just had this issue, I was able to fix it by running sudo raspi-config, then going to Advanced, then Change Hostname, then Reboot. / Give it a try. / Darle la opcion de visualizacion global

You may need to enable SSH, however, you are receiving a prompt, so most likely is already active, just in case:

$ sudo update-rc.d ssh enable

if security is high, edit /etc/ssh/sshd_config

$ sudo nano /etc/ssh/sshd_config / # comment / #PermitRootLogin without-password / # and add / PermitRootLogin yes / # and also / #StrictModes yes / StrictModes no

then, restart the ssh service:

sudo invoke-rc.d ssh restart / # or / sudo service ssh restart

Script at init:

miscript.sh

#!/bin/bash / ### BEGIN INIT INFO / # Provides: blabla / # Required-Start: $syslog / # Required-Stop: $syslog / # Default-Start: 2 3 4 5 / # Default-Stop: 0 1 6 / # Short-Description: blabla / # Description: / # / ### END INIT INFO / python /root/proyectosPython/blinky.py & / exit 0

# Ejecutar un script en el arranque de linux

Para conocer un poco como funcionan los runlevel del sistema, podemos leer Como funcionan los runlevel del sistema.
Una vez ya sabemos como funcionan los runlevel, procedemos a explicar como ejecutar un script o programa al arranque del sistema.
1) Damos permiso de ejecución al script.
#sudo chmod -x miscript.sh # u+x +777
2) Copiar el script a la carpeta /etc/init.d/
#sudo cp miscript.sh /etc/init.d/
3) Lo convertimos en daemon, es decir, que se ejecute al inicio de la sesión.
#sudo update-rc.d miscript.sh defaults
Esto creara los enlaces simbólicos automáticos para todos los runlevels, así dependiendo del tipo de inicio, arrancara nuestro script, y ya lo tendremos echo.
Solución al error “insserv: warning: script X missing LSB tags and overrides”
Por ejemplo si haces
update-rc.d jailkit defaults
te dará el siguiente error:
update-rc.d: using dependency based boot sequencing
insserv: warning: script 'K01jailkit' missing LSB tags and overrides
insserv: warning: script 'jailkit' missing LSB tags and overrides
Ahora bien, si editas el archivo en cuestión (en este caso /etc/init.d/jailkit) y pones al principio del todo lo siguiente:
#!/bin/bash
### BEGIN INIT INFO
# Provides: blabla
# Required-Start: $syslog
# Required-Stop: $syslog
# Default-Start: 2 3 4 5
# Default-Stop: 0 1 6
# Short-Description: blabla
# Description:
#
### END INIT INFO
Comandos para averiguar el PID:

$ ps -xj / $ ps ax | grep 527 / $ kill -term 527 #mata el daemon

BLINK LED:

#EJEMPLO DE BLINKING CON RASPBERRY PI / #Escrito por Gl4r3 / import RPi.GPIO as GPIO #importamos la libreria y cambiamos su nombre por "GPIO" / import time #necesario para los delays / #establecemos el sistema de numeracion que queramos, en mi caso BCM / GPIO.setmode(GPIO.BCM) / #configuramos el pin GPIO17 como una salida / GPIO.setup(17, GPIO.OUT) / #encendemos y apagamos el led 5 veces / for i in range(0,5): / GPIO.output(17, GPIO.HIGH) / time.sleep(1) / GPIO.output(17, GPIO.LOW) / time.sleep(1) / GPIO.cleanup() #devuelve los pines a su estado inicial